## Slide 1: DLA hardware
Yi Li
2017/11/30

## Slide 2: Outline
Performance/bandwidth Requirement for CNNs
Compression for bandwidth
Computing reduced for performance

## Slide 3: Outline
Performance/bandwidth Requirement for CNNs
Compression for bandwidth
Computing reduced for performance

## Slide 4: Performance/bandwidth Requirement for CNNs
 | Alexnet | GoogLeNet(v1) | Tiny YOLO | YOLO v2
MACs | 724M | 1.43G | 3.5G | 17.5G
Weight Num | 61M | 7M | 15.1M | 48.3M
Weight Size (16bits) | 122MByte | 14MByte | 30.2MByte | 96.6MByte
DDR bandwith | 9.6GBytes/4 | 9.6GBytes/4 | 9.6GBytes/4 | 9.6GBytes/4
MACs computing | 1024 | 1024 | 1024 | 1024
Embedded Freq | 600MHz | 600MHz | 600MHz | 600MHz
FPS (bandwith) | 20 | 171 | 79 | 25
FPS (computing) | 848 | 429 | 175 (actually 5 fps in sirius @800MHz) | 35

## Slide 5
Performance/bandwidth Requirement for CNNs
Bandwidth
Computing
Sparsity

## Slide 6: Performance/bandwidth Requirement for CNNs
Static (Weight): Quantization

## Slide 7: Performance/bandwidth Requirement for CNNs
Static (Weight): prune
Alexnet | conv1 | conv2 | conv3 | conv4 | conv5 | fc6 | fc7 | fc8
sparsity | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.005 | 0.005 | 0.005

## Slide 8: Performance/bandwidth Requirement for CNNs
Alexnet | pool1 | pool2 | conv3 | conv4 | pool5 | fc6 | fc7
sparsity | 0.875 | 0.467 | 0.291 | 0.32 | 0.296 | 0.046 | 0.072
Dynamic (feature map)

## Slide 9: Outline
Performance/bandwidth Requirement for CNNs
Compression for bandwidth
Computing reduced for performance

## Slide 10: Compression for bandwidth
value | 1 | 0 | 2 | 3 | 0 | 0 | 0 | 0 | 4
value | 1 | 2 | 3 | 4
indx | 0 | 2 | 3 | 8
value | 1 | 2 | 3 | 0 | 4
Nxt nz dis | 1 | 0 | 3 | 0 | …
Uncompressed
Conventional compress
Proposed compress
Indx width is undetermined and large
Indx width is determined (2bit or 4bit)

## Slide 11: Compression for bandwidth
128bit
16bit x 8
8bit x 16
128bit
(16bit+4bit) x 6
(8bit+4bit) x 10
If sparsity = 0.005, compress ratio 16bit : 1/(0.005*8/6)=150
8bit: 1/(0.005*16/10)=125
If sparsity = 0.5, compress ratio 16bit : 1/(0.5*8/6)=1.5
8bit: 1/(0.5*16/10)=1.25

## Slide 12: Compression for bandwidth

## Slide 13: Outline
Performance/bandwidth Requirement for CNNs
Compression for bandwidth
Computing reduced for performance

## Slide 14: Computing reduced for performance
Static (Weight):
Need bright thought

## Slide 15: Computing reduced for performance
Static (Weight):
Generator can eliminate zero weight of input channel (granularity 16 )

## Slide 16: Computing reduced for performance
Static (Weight):
Generator can eliminate zero weight of output channel (granularity 16 )

## Slide 17: Computing reduced for performance
Dynamic (feature data):
How to skip zero value computing efficiently?

## Slide 18: Computing reduced for performance
Dynamic (feature data):
Add 4bit/2bit in each mem for indicating next non-zero value

## Slide 19: Computing reduced for performance
Dynamic (feature data):
Divide mem into small width

## Slide 20: Computing reduced for performance
Dynamic (feature data):
PE width=8 | pool5 | fc6 | fc7
cycle | 132 | 29 | 33
original cycle | 144 | 64 | 64
Cycle reducing | -8.3% | -54.7% | -48.4%
PE width=16 | pool5 | fc6 | fc7
cycle | 140 | 41 | 50
original cycle | 144 | 64 | 64
Cycle reducing | -2.7% | -35.9% | -21.9%

## Slide 21: THANKS ! Q & A