## Slide 1: DLA hardware
Yi Li
2017/12/14

## Slide 2: Outline
Technical topic
Discussion

## Slide 3: Technical topic
Technical topic
1)compress/decompress/data format
2)tile/padding
3)input channel partition
4)skip zero
5)pooling/lrn memory mechanism
6)DMA implement
7)Image input
8)software control
9)CNN layer type
10)generator

## Slide 4: Technical topic
bit | expand bit | date num per axi | max decompress num per axi
16 | 3/4/5 | 6/6/6 | 384 Bytes
8 | 3/4/5 | 11/10/9 | 288Bytes
4 | 3/4/5 | 18/16/14 | 224Bytes
2 | 3/4/5 | 25/21/18 | 144Bytes
1 | 3/4/5 | 32/25/21 | 84Bytes
1)compress/decompress/data format

## Slide 5: Technical topic
2)tile/padding
How to divide tiles better？
Choose which block add padding better?
very very very wide

## Slide 6: Technical topic
2)tile
principle | reason
all input channel | if not all input channel, we should add temp register to preserve temp accumulation value
at least one kernel for all input channel | If not meet one kernel for input channel, we should also add temp register to preserve temp accumulation value

## Slide 7: Technical topic
2)tile
Need all input channels

## Slide 8: Technical topic
2)tile
Need at least one kernel

## Slide 9: Technical topic
2)tile
Featuremin = input_channel * kernel_x * kernel_y
Weightmin = input_channel * kernel_x * kernel_y
General tile partition strategy,
(Total- Featureall)/2 = Weight
input_channel * kernel_x * kernel_y * output_channel(int x16) = Weight

## Slide 10: Technical topic
2)padding
padding | drawback | advantage
CDMA | CBUF space wasting | Regular data format on DDR
CSC |  | Regular data format on DDR
BDMA | Being aware of next layer tile partition | 

## Slide 11: Technical topic
2)padding
block | function
CDMA | Transfer boundary data from DDR to CBUF
CSC | compute conv with adding padding

## Slide 12: Technical topic
2)padding
From parameters, CDMA and CSC knows how to transfer data and add padding

## Slide 13: Technical topic
3)input channel partition
case | Input channel | Output channel | Kernel size_x | Kernel Size_y | Feature Size_x | Feature Size_y
Alexnet conv5 5x5 | 192 | 256 | 3 | 3 | 13 | 13
weight
data
clk
16
27
9
25
27
1
16

## Slide 14: Technical topic
3)input channel partition

## Slide 15: Technical topic
3)input channel partition
input channel | output channel | kernel_x | kernel_y | feature_x | feature_y
160 | 64 | 3 | 3 | 13 | 13
weight
data
clk
16
18
9
25
18
1
4
Total time: （9*18*16 + 1*18*25) * 4 = 12168
Utilization: 62.5%

## Slide 16: Technical topic
3)input channel partition
input channel | output channel | kernel_x | kernel_y | feature_x | feature_y
160 | 64 | 3 | 3 | 13 | 13
weight
data
clk
16
45
9
25
45
1
1
Total time: （9*45*16 + 1*45*25) * 1 = 7605
Utilization: 100%

## Slide 17: Technical topic
3)input channel partition
input channel | output channel | kernel_x | kernel_y | feature_x | feature_y
160 | 64 | 3 | 3 | 13 | 13
1
2
3
1
2
3
4
5
…
Require sub mem read

## Slide 18
4) skip zero
How to skip zero value computing efficiently?
Technical topic

## Slide 19
Add 4bit/2bit in each mem for indicating next non-zero value
Technical topic
4) skip zero

## Slide 20
4) skip zero
Divide mem into small width
Technical topic

## Slide 21
4) skip zero
Technical topic
2 conditions :
Distributed accumulation
Distributed mem
The less Feature num, the more efficiency in each cycle
costs :
Add extra bits on memory
Add extra interface between CSC and CBUF for indicating current computing index (4bit-6bit per computing engine)

## Slide 22
5)pooling/lrn memory mechanism
Technical topic
After convolution, feature computing order

## Slide 23
5)pooling/lrn memory mechanism
Technical topic
pooling:
1)need add padding, stride
2)Min buffer size require: pool_size_y*output_feature_x*16

## Slide 24
5)pooling/lrn memory mechanism
Technical topic
lrn:
1)need add padding, stride
2)Min buffer size require:
depth*output_feature_x*output_feature_y

## Slide 25
6)DMA implement
Technical topic
BLOCK | FUNCTION | object
CDMA | 1) send read request to DDR 2) add extra bit for skipping zero | Decompress -> ->CSC
BDMA | send write request to DDR send write request to CBUF adjust data format | CMAC/SDP/PDP/CDP/RUBIK -> ->compress
How to
1) Memory consistency for master/slave AXI

## Slide 26: Discussion
1.Different bits
2.Run-length coding
3.Buffer/Queue

## Slide 27: Discussion
1.Send read request to DDR(tile boundary data)
2. Write CBUF
3. Compute skip zero distance

## Slide 28: Discussion
1.Distributed memory
2.Extra bits for skipping zero value

## Slide 29: Discussion
1.Adding padding
2.Control data sequence for CMAC
3.Skip zero and send signal for CMAC (Add extra interface)
4.Weight Index mode

## Slide 30: Discussion
1.CMAC computing
2.Input channel partitioning

## Slide 31: Discussion
1. Can reload data from CBUF directly

## Slide 32: Discussion
Adjust data format
Transfer data to CBUF
Transfer data to DDR

## Slide 33: Discussion
Compress feature data

## Slide 34: Discussion
Store input configure (more than 3 group buffer for supporting 3 layers. TBD)
Control others blocks and process interrupt

## Slide 35: Discussion
10) Image input
Only 3 input channel, if 8bits pixel, (total 1024bit, 256bit each engine), utilization only 10%
Data format in DDR. Which block is in charge of data reorder. (DMA?)
7)software control
Distributed register set
Centralized register set
8)CNN layer type
All mainstream, Alexnet/googlenet/resnet
FCN/segnet/mask RCNN
YOLO/SSD/faster-rcnn
9)Generator
Network parser/Instruction/data transfer

## Slide 36: Discussion
SPEC
verification
C-model
rtl
algorithm
implementation

## Slide 37: THANKS ! Q & A