## Slide 1: DLA HW Specification review meeting
DLA group
2018-1-8

## Slide 2
讲演提纲
已有的深度学习加速芯片
Our DLA HW SPEC/ASIC performance
Feature list
Feature list to be done
System diagram
DLA internal diagram
子模块架构
  卷积buffer
  MAC array/CDP
  SDP/PDP
  SCU
软件议题
FPGA议题
数字电路前端设计流程

## Slide 3
已有的深度学习加速芯片
厂家名称 | 芯片名称 | 工艺（nm） | MAC算力（TOPS） | MAC数量 | 功耗 | 工作频率（Mhz） | die size（mm2） | 发布时间
华为海思 | 麒麟970 | 10 | 1.92T |  | N/A | N/A | N/A | 2017.9
Google | TPU | 28 | 92T@8bit | 65K | 40W | 700 | 331 | 2016.5
Google | TPU2 | 12 | 180T |  |  |  |  | 2017.5
比特大陆 | BM1680 | 28 | 2T@FP32 |  | 30W |  |  | 2017.4
比特大陆 | BM1682 | 28 | 3T@FP32 |  | 30W |  |  | 2017.12
地平线 | 征程/旭日 | 40 | 1T |  | 1.5W |  | BGA14X14 | 2017.6
深鉴科技 | 听涛 | 28 | 4.1T |  | 1.1W |  |  | 2017.11
瑞芯微 | RK3399Pro |  | 2.4T |  |  |  |  | 2018.1

## Slide 4
Our DLA HW SPEC
TSMC 28nm
Die size：2mm2，density 60%, 4M equiv ASIC gate
On chip convolution buffer: 2MB
Max Power: 1W
MAC #: 1024 INT16 or 16K INT4/2/1
MAC Utilization：90-100% （except input or FC layer）
Max Frequency: 1GHz （Typ 700MHz）
Max OPS: 32T for INT4/2/1, 8T for INT8, 2T for INT16
FPGA Frequency: 300MHz on VU440

## Slide 5
ASIC Performance Estimation
Max OPS: 2T for INT16, 8T for INT8, 32T for INT4
Without weight compression, DDR efficiency not considered
GoogleNet (1 frame needs 3.2GOPS)
  2560 frame/s, 20GB/s DDR (8bit feature/weight)
  10000 frame/s, 40GB/s DDR (4bit feature/weight)
Yolo v2 ( 1 frame 35GOPS)
  228frame/s, 12.8GB/s (8bit feature/weight)
  914frame/s, 25.6GB/s (4bit feature/weight)

## Slide 6
DLA Feature List
Different 1/2/3D convolution layer
  Direct/Image-input/Batching
  Deconvolution
  Atrous/dilated convolution
Hybrid precision MAC supporting INT16/8/4/2/binary
On-chip convolution buffer up to 2MB
Various activation layer
  HW: ReLu/PReLu/Leaky ReLu/CReLu/RReLu/ReLu6
  LUT: ELU/SELU/tanh/sigmoid
  SW: softmax/softplus/softsign
Pooling (2D/3D)
  Max/min/average with different stride
Local Response Normalization
Elementwise operation
  Batch Normalization, scale, bias add

## Slide 7
DLA Feature List to be done?
Winograd
Depthwise_conv2d
Pooling 3d
Dropout

## Slide 8
Application System Diagram

## Slide 9
DLA internal Architecture

## Slide 10
Convolutional Buffer

## Slide 11
MAC Array

## Slide 12
SDP

## Slide 13
PDP

## Slide 14
CDP

## Slide 15
SCU

## Slide 16
软件相关议题
神经网络生成器
  支持多种框架：tensorflow、tensorflow Lite、Caffe
  DLA执行指令的生成
软件API
  TEngine
  Android NNAPI
  Halide
中间表示层
  LLVM （ Google XLA ）
  NNVM/TVM

## Slide 17
FPGA相关议题
Demo应用
  人脸检测（Yolo/SSD），无人机
  人脸识别（FaceNet/mobilenet），无人机
  手势识别 (C3D fusion), 无人机
  物体识别（Yolo、Google），无人机/扫地机

## Slide 18
设计进度安排

## Slide 19
数字前端设计流程
Design stage | Tools | Output
Design Specification | Word / excel /Visio | PDF file describes the system function and architecture
Algorithm modeling | Matlab / gcc/ VS | Documents describe the algorithms. C or matlab code
RTL design | Synplify / DC /Spyglass | Verilog HDL code
Function verification | VCS Veloce | RTL Test case list and the status of each test case Code coverage generated by VCS Code coverage generated by Veloce
FPGA prototype | Synplify/ Vivado QuartusII/ PlayerPro | FPGA test case list and the status of each test case
ASIC synthesis | DC / FM Conformal Spyglass | Netlist file ready for backend design Pass Formal verification Timing/area statistics Lint/CDC clear
Power estimation | VCS / PrimeTimePX | Average and peak power of typical application