## Slide 1: Ultrafast FPGA Prototyping Flow

## Slide 2: Outline
FPGA structure
  LUT, RAMB, DSP, IO, CLOCK
Prototyping flow
  Synplify synthesis
  Vivado implement
Polestar verification plan
  Hardware structure
  System-level verify tasks

## Slide 3: FPGA Structure

## Slide 4: FPGA structure -- logic blocks
6-input LUT is actually a 64x1 RAM
Flip-flop consists of 5 NAND gates
A SLICEM contains 4 LUT6, 8 FFs and cascading logic
  Implement combinatorial functions, small RAM or shift register
A SLICEL contains 4 LUT6
  Implement combinatorial logic
Two slices combined into a CLB
  The basic logic cells in FPGA array

## Slide 5: FPGA structure -- memories
Distributed RAM
  Small memories instantiated by SLICEM
Block RAM
  Configurability: dedicated, dual-ported synchronous 36Kbits RAM can be configured for different width and depth
  Synchronous of each port for different clock rate
  FIFO logic

## Slide 6: FPGA structure -- DSP slice
DSP48E1: dedicated, configurable and low-power
  25x18 bit multiplier
  48-bit accumulator
  30x25 bit pre-adder
Map objects in many modes
  wide dynamic bus shifter
  memory address generator
  wide bus multiplexer

## Slide 7: FPGA structure -- Clock network
MMCM is a configurable clock generation unit
Clock distribution resources
  Global clocks, high fan-out, low distribution delay, can be driven by global clock buffer and MMCM output
  Reginal clocks (a region is defined as any area that is 40 IOs and 40 CLBs)
  IO clocks, serve only IO logic and SERDES circuits

## Slide 8: FPGA structure -- IO pins
40 pins consist of one bank which has a common Vcc
Single-ended IO uses CMOS push/pull output structure and can be put into high-Z state
  Can be configured as either combinatorial or registered
  IO delay (0 ~ 78ps) and drive current ( 2mA ~ 24mA)
Differential IO with LVDS standards supported

## Slide 9: Prototyping Flow

## Slide 10: Prototyping Intro
benefit
limitation
High performance and accuracy
Real-time/long-time dataflow within the real world
Hardware-software integration
Out-of-lab demonstration
Not a simulator or debugger
Iteration cycle is long
ASIC is larger than FPGA
ASIC is faster than FPGA
Analog PHY shall be removed

## Slide 11: Prototyping Flow
RTL modification
Manual partition for multi-FPGAs (optional)
Synthesis sub-modules with Synplify
Add constraint for PAD, clock, IO
Place&Route with Vivado
Debug and ECO

## Slide 12: RTL Modifications
Top-level wrapper (pin share, PAD, PLL)
TSMC gate-level netlists
SOC memories, DesignWare
Build-in self test (BIST) is not required
Gated clocks
Complex generated clocks

## Slide 13: RTL Modifications -- Gate Clock Conversion
Identify the base clocks in SDC
Insert black-box for combinational loop
For non convertible clock
  Manually add clock buffers, PLLs for balancing
  Use high frequency global clock to detect gated clock edge as new clock enable
  Directly assign output clock to input clock with gate logic bypassed

## Slide 14: RTL Modifications -- Block RAMs
MASK_BIT | Block RAM utilization
1 | 
4 | 
8 | 
32 | 

## Slide 15: RTL Modifications -- Top/Partition Wrapper
FPGA TOP Wrapper
  Instantiate PLL and clock buffers, DDR3/DDR4 , ROM and inout IO connection
  Instantiate Black-Box for sub-modules
  Instantiate SOC_TOP without analog PHY
Partition Wrapper
  Standalone, large size, low performance IPs
    CEVA, HEVC
  Need pin mux logic for insufficient IOs between FPGAs
  Workaround to avoid partition
    Several special version for different data path

## Slide 16: Bottom-up Synthesis -- Synplify Premier
Netlist generation
  Generate netlist for sub-modules, parallel synthesis can be finished in a day
  Generate netlist for TOP wrapper
  Only correlative module and TOP wrapper need to resynthesize when there are modifications
Time: 10m:41s
Freq. 123.9MHz
Time: 2m:33s
Freq. 50MHz

## Slide 17: Implementation -- Vivado P&R
Project tcl based flow: check DRC report at each stage
  Link design: link all netlist from synplify
  Opt design: optimized with netlist
  Incremental check point read out (optional)
    Less than 5% modifications can save half implementation time
  Place design
  Route design
Timing constrain is very important
  Clock groups / Cross clock domain
  False path / multi-cycle path
  Input / output delay
  DON’T over constrain; DON’T floorplan

## Slide 18: Implementation -- Vivado ECO
Applications
  Change properties of LUTs (default value of Register; clock phase of MMCM)
  “UpdateMEM” can update bit files with MMI and ELF data
  Swap/move cells, disconnect/re-route nets
  Replace/add debug probes
  ECO can be finished within about 1 hour

## Slide 19: Real-time Debug -- ILA/JTAG
With Vivado logic analyzer
  Capture probe waveform
  Set kinds of trigger condition
With JTAG interface
  Read out all registers and memories

## Slide 20: Polestar Prototype Plan

## Slide 21: Hardware Structure

## Slide 22: Software tasks
No. | Description | Status
CSI2 #1 | Different data lanes: MIPI 1, 2, 4lane | 
CSI2 #2 | Different sensor numbers: Senor 1, 2, 4, 8 | 
CSI2 #3 | Different virtual channel: VC0, 1, 2, 3 and combination | 
CSI2 #4 | Different data type: RAW8, RAW10, RAW12, RGB | 
VIF | Different image resolution: VGA, 720P, 1080P, 4K2K | 
H264 | Encode and decode for different resolution | 
ISP | Reserved | 
DSI #1 | MIPI 1, 2, 4 lane | 
DSI #2 | Resolution: 720P, 1080P | 
DSI #3 | Video mode, Command mode | 

## Slide 23: System evaluation
Hardware
  About 60% LUT, 80% DSP, 70% RAMB resources of VU440FLGA2892
  3 daughter boards need PCB produce
  2 VU440 platforms (already exists)
Software
  Python 3.6 with USB control
Time estimate
  First prototype needs about 2 weeks
  Compile once a day
  ECO 3 times a day
  Traversal verification tasks several times a day

## Slide 24: Thank you