## Slide 1: Veloce used in Sirius
Jianzhong Zhang

## Slide 2: Content
Introduction
Veloce Flow
Veloce used in Sirius Verification
Debug Tips

## Slide 3: Introduction about Veloce Emulator
Why do we choose Veloce Emulator?
Traditional EDA software simulation is too slow for large SOC.
FPGA signal visibility is poor.
Veloce Emulator is 1000 times faster than EDA simulation and all signal visible.It helps us to verify our chip conveniently and quickly.

## Slide 4: Introduction about Veloce Emulator
Feture of Veloce Emulator
High-capacity and high-speed
100% signal visibility and strong ability of debug
Compile quickly
  Multiple user and multiple modes

## Slide 5: Introduction about Veloce Emulator
Veloce2 Quattro

## Slide 6: Veloce Flow
Library unit mapping
  Clk/memroy
Compilation
  Analyzer
  Rtlc
  Velsyn
  Velcc
  Velgs
  Ssrcc
Simulation
  Make build
  Make sim
Debugging

## Slide 7: Veloce Flow
What is TBX(TestBench eXpress)
  An environment/infrastructure where
  —the design runs on a hardware platform (Veloce)
  —the testbench (C or SystemCor SV) runs on a software platform (workstation)
  —the two communicate through a transaction interface
  A transaction-based co-modeling environment
  —as opposed to a pin/cycle-based co-simulation environment
  Uses SystemVerilog-DPI (SV-DPI) for transaction-based data transfer across workstation and hardware

## Slide 8: Veloce Flow

## Slide 9: Veloce Flow
Make build
  Velhvl:add the source language of HVL in veloce.config
    -comp –hvl [c|systemc|questa]
  There are two ways to compile the HVL
    -velcomp –task hvl
    -velhvl
  It is the command for all the hvlcompilations
    -velhvl–cfiles <user C/C++ files>
  Same command for all type of hvlsource language except Questa

## Slide 10: Veloce Flow
  Automated C Compilation
  Manual C Compilation

## Slide 11: Veloce Flow
  Compiling for Dynamic loading
  Questa Mode HVL Compilation

## Slide 12: Veloce Flow
Make sim
  All use modes use velrun
    -velrun
    -velrun –c
    -velrun –gui
  Vsim used for Questa test-benches
  Velrun:Platform TCL commands

## Slide 13: Veloce used in Sirius Verification
For Artosyn project Sirius, Veloce Emulation flow is to run real use case for verification. To use Veloce resources efficiently, we deliver Veloce images in 4 different types, targeting different scenarioes.
From Build 1 to Build 4 the included designs become more and more. One of the target is to keep image small enough for Veloce limited AVBs and concurrent usage.
  Build 1: Minimal System
  Build 2: A7 plus CEVA
  Build 3: Video Case
  Build 4: Wireless Tx/Rx

## Slide 14: Veloce used in Sirius Verification
Example(build3)

## Slide 15: Debug Tips
  scompile test_case –vel –docompile
  cd to tmpdir/test_case_VEL
  make build
  make sim

## Slide 16: Debug Tips
  Run.do/run.tcl
    memory upload/download
    trigger download
    reg force value
    xwave on
UART

## Slide 17: Debug Tips
  Wave
    Velview

## Slide 18: Debug Tips
  Wave
    Visualizer

## Slide 19: Debug Tips
  Codelink
    Software running state,break point,one step,one function
    Memory value(DDR)
    Register value

## Slide 20: Debug Tips
  Trigger file + HWtrace

## Slide 21: Q&A
Thanks. Q&A