## Slide 1: Sirius Bring up Report
Song Pan 2018-02-09

## Slide 2: Total Bring up time & resource summary
Total bring up time 12 days from 1/29/2018 to 2/9/2018.
Total bring up platforms 7x socket board and 2x solder board with 9x test PC.
Total bring up resource : SOC/Analog/BB/SE/ISP/Video/SW/SAE/IT team

## Slide 3: Total Bring up user cases
ROM boot from QSPI flash, U boot/SPL/ Kernel success
ROM boot from eMMC flash
1x MIPI sensor input-> ISP-> DE->DVP-VGA
HDMI RX -> DE->DVP-HDMI TX 1080p@60
BB TX -> RX in mode B

## Slide 4: Total Bring up items summary
Fail item | 0 | 0.00%
Not done item | 5 | 3.42%
Pass item | 141 | 96.58%
Total item | 146 | 100.00%

## Slide 5: Bring up detail list - 1
IP | bring up item | Status | 
Analog block | 1. Finish all PLL frequency test, all PLL default frequency is OK. | Pass | 
 | 2. Finish all ABB DC test, all value meet SPEC. | Pass | 
 | 3. Successfully pass AD-DA loop test flow. | Pass | 
 | 4. Finish SAR ADC function test. | Pass | 
 | 5. Temp sensor pass 1 temprature point measure(42 degree). | Pass | 
 | 6. Finish PVT sensor function test. | Pass | 
 | 7. Finish DSPPLL 0/1/2 fine test and DC test. | Pass | 
 | 8. Finish AD/DA fine test and performance test. | Pass | 
 | 9. Audio PLL locked using by HDMI_RX. | Pass | HW mode is not correct, but workaround by SW mode.

## Slide 6: Bring up detail list - 2
DDR | 1. 1200Mbps based on socket board. DDR R/W test pass. | Pass
 | 2. 1600Mbps based on socket board. DDR R/W test pass. | Pass
 | 3. 2400Mbps based on socket board. DDR R/W test pass. | Pass
 | 4. Inline ECC pass. | Pass
QSPI | 1. A7 boot from ROM+QSPI flash successfully. | Pass
 | 2. A7 boot from QSPI flash successfully. | Pass
 | 3. Sirius image of nor flash is ready. Path: \\viewss\import\Software\Sirius\ImageRelease\BringUp\Day1 artosyn-veloce_build1-sirius-001-d-0.0.0.1.spi.nonsec.0129.img | Pass
 | 4. QSPI flash quad read function pass. | Pass
 | 5. QSPI program is passed. | Pass
 | 6. 100MHZ work frequency is passed. | Pass
BB | 1. BB register configuration PASS. Successfully sending out sine wave. | Pass
 | 2. Passed functionality test of mode b (BR/SLOT TX/RX). | Pass

## Slide 7: Bring up detail list - 3
HDMI_RX | 1. SPI debug tool read/write register is OK. | Pass
 | 2. HDMI video function is OK. | Pass
 | 3. Audio PLL is not stable. Audio function is OK with SW program mode. | Pass
DVP | 1. SPI debug tool read/write register is OK. | Pass
 | 2. Use HDMI as video source, and dvpo control function and display, mode select to BT601 16 bit SDR mode, the pixclk/hs/vs/de is normal. | Pass
 | 3. RGB2VGA display is ok @1080p 60fps, dvp rgb888 mode is ok. | Pass
HEVC | 1. Power on HEVC. The current adds 15mA. | Pass
 | 2. SPI debug tool can read/write HEVC register normally. | Pass
 | 3. 1080 case. HEVC encoder encode 10 frames(Gop type IPPPP). Upload code stream and use software tool to display picture normally. | Pass
 | 4. 4K(3840X2160) case is passed. | Pass
 | 5. HEVC decoder 1080P case is passed. | Pass
 | 6. HEVC decoder 4K(3840X2160) case is passed. | Pass

## Slide 8: Bring up detail list - 4
DE | 1. DE outputs pclk/vsync/hsync/de normally. | Pass
 | 2. DE interrupt is OK. | Pass
 | 3. DE can use DVP_RGB_TX to output colour_bar's picture. Test case: 1920X1080@60fps, core_clock 400Mhz, AXI_clock 500Mhz, pclk 148.5Mhz. | Pass
MIPI_RX | 1. Register read/write is OK. | Pass
 | 2. Register default value is OK. | Pass
 | 3. The case of config( 2lane_sensor, 640Mbps/lane, raw10 + MIPI_RX + VIFBP) is ok and the data in DDR is right proved by ISP team. | Pass
 | 4. PASS Case: 2lane_sensor , 640Mbps/lane ,raw10 + MIPIRX + ISPIF+ ISP; | Pass
 | 5. Test 8x MIPI relative PAD with the config of <4lane_sensor , 640Mbps/lane ,raw10 + MIPIRX + VIFBP+ ISP> and the firmware of LLLI is ok. | Pass
ISP | 1. ISP power off status switch to power on and function is passed at 500Mhz. | Pass
 | 2. Read/write register is passed. | Pass
 | 3. ISP read raw10 data from DDR ping/pong frame buffer and output YUV420 to DDR is passed. | Pass
 | 4. ISP interrupt is passed. | Pass
 | 5. Sensor -> VIF -> DDR -> ISP -> DDR data path is passed. ISP input video: 2112X1568@20fps, ISP output YUV420 1920X1024@20fps. | Pass
 | 6. Sensor->VIF->ISP->Display pass. | Pass
 | 7. ISP 200MHZ~666MHZ frequency point is passed. | Pass
 | 8. ISP software reset and release is passed. | Pass

## Slide 9: Bring up detail list - 5
CEVA | 1. Power protection and power on 4 cores are OK. The current increases about 7mA when one core is power on. | Pass
 | 2. SPI reading the APB registers in ceva_harden_subsystem and the CPM registers in ceva core0 is OK. | Pass
 | 3. Using JBOX with its firmware v114(with signal "RTCK") and v119(without signal "RTCK") to connect the ceva core0 in chip with toolbox to debug is OK. Simple programme has been tested. The results of the calculation are right. Also, using ceva core0 to configure the APB registers are OK. | Pass
 | 4. The UART in ceva_harden_subsystem can display normally. The baut rate calculation has been updated in the GIT. | Pass
 | 5. When the non-overshoot frequency control in PLL is set, the maximum frequency can reach 1.16GHz. | Pass
 | 6. When it is not set, the maximun frequency can reach 1.12GHz | Pass
CA7 | 1. CA7 can boot from ROM+QSPI and print information through secure uart. | Pass
 | 2. CA7 can boot from QSPI directly and print information through secure uart. | Pass
 | 3. CA7 can be debuged through JLINK. | Pass
 | 4. Ca7 can work to 1.2Ghz without opening non-overshoot. | Pass
 | 5. Ca7 can work to 1.43Ghz with opening non-overshoot. | Pass
 | 6. Ca7 can work to 1.43Ghz using ca7_pll glitch free mux. | Pass
 | 7. Register can be accessed by SPI debug and JLINk. | Pass
 | 8. Booting linux kernel from DDR with L1/L2 cache enabled is ok. | Pass
 | 9. Power down one cortexa7core which is in WFI state in 1Ghz decreases about 1mA. | Pass
 | 10. CPU running points: one core 1420 @ 500Mhz; one core 2842 @ 1Ghz; one core 3410 @ 1.2Ghz; | Pass

## Slide 10: Bring up detail list - 6
EMMC | 1. can read/write EMMC device but with a error flag | Pass | need further dig. Waive this error, no impact function.
 | 2. There is some problem with booting from EMMC. | Pass | boot OK when fix PCB power supply sequence.
 | 3. Access register case is OK; | Pass | 
 | 4. EMMC SDR50 is passed. | Pass | 
M7 | 1. M7 boot from qspi flash directly (print log via uart0 and release M7) OK. | Pass | 
 | 2. M7 boot from ITCM (print log via uart0) | Pass | 
 | 3. M7 frequency switch test pass; 300/400/500Mhz. | Pass | 
USB | 1. controller/phy/local regs test ok on EK board | Pass | 
 | 2. link state can run into U0 | Pass | 
 | 3. observe usb2.0 port chirp handshake to HighSpeed through the protocol analyzer. | Pass | 
 | 4. usb2.0(480Mbps) and usb3.0(5Gbps) massive storage device can be detected and control/bulk transfer pass. | Pass | 

## Slide 11: Bring up detail list - 7
GMAC | 1. Access register case pass; | Pass
 | 2. Check gmac mdio interface is OK | Pass
 | 3. Link ok. Can transfer data package. | Pass
SMMU | 1. Access register through Jlink is ok. | Pass
sec | 1. All registers read/write ok on EK board, | Pass
 | 2. release troot reset, and its register test ok | Pass
 | 3. test secure timer/watch dog function ok | Pass
 | 4. SPACC AES-256 in CBC mode encrypt&decrypt pass | Pass
 | 5. PKA RSA-2048 encrypt&decrypt pass | Pass
 | 6. TRNG random reseed and random number gen pass | Pass
 | 7. tRoot firmware boot pass with all 0 keys(non programed otp) | Pass
 | 8. tRoot firmware boot pass with specific key(programed otp) | Pass
 | 9. RSA encrypt and decrypt is ok. | Pass

## Slide 12: Bring up detail list - 8
I2S | 1. Access register case pass | Pass
 | 2. Pass the tx of i2s0, i2s1, i2s2, i2s3 1bit mode with oscilloscope | Pass
TYPC | 1. TCPC registers test ok on EK board;Other registers need the internal FW loading and TCPC controller work normal. | Pass
 | 2. TypeC PHY cmn_ready assert, indicating common modules are powered up, calibrated and the PLL has locked | Pass
 | 3. DP PLL in RBR(1.62Gbps), HBR(2.7Gbps) and HBR2(5.4Gbps) with 1lane, 2lane and 4lane locked. | Pass
 | 4. TypeC USB3.0 Host enumeration and Bulk in/out transfer work normally. | Pass
 | 5. DP PLL in RBR(1.62Gbps), HBR(2.7Gbps) and HBR2(5.4Gbps) with 1lane, 2lane and 4lane locked. | Pass
PCIE | 1. set register device_type to rc mode, set app_ltssm_enable and seems pcie gen2 link up is ok according to link status register read value. | Pass
 | 2. set iatu function for cfg tlp, cfg read for device vendor id and cfg write for bar0 is ok. | Pass
 | 3. set device status_command_reg[2:0]=3'b111, bar3=32'hff8e0000 (according to driver doc), and now mem rd/wr tlp works. | Pass

## Slide 13: Bring up detail list - 9
DMAC | 1. ddr transfer with top_dmac case pass; | Pass
 | 2. test the ceva_dmac with sram, and the ceva_dmac transfer is OK; | Pass
UART | 1. Uart0 print log successfully. (including pin-share configure) | Pass
 | 2. UART-1 transfer data with DMA feature pass | Pass
SPI | 1. SPI master 1/2/3 basic transmission function pass, at 25MHz. | Pass
 | 2. DMA mode. | not_done
PWM | 1. Access Timer0/1/2 registers via SPI debug port, successfully | Pass
 | 2. PWM0~9 function pass. | Pass
I2C | 1. I2C 2/4 basic function pass. | Pass
 | 2. DMA mode. | not_done
WDT/Timer | 1. Access WDT/TImer registers via SPI debug port, successfully | Pass
 | 2. WDT/Timer basic function pass | Pass

## Slide 14: Bring up detail list - 10
AHB_DMA | 1. run AHB_DMA case in M7 core; | Pass
 | 2. transfer 256 byte datas from flash to sram, testcase passed. | Pass
 | 3. AHB_DMA transfer big amount of data pass, from flash to sram, and from sram to sram. Verify the async H2H bridge indirectly. | Pass
CS | 1. Coresight can auto detect the topology of our SoC successfully; (remove the connection to BB) | Pass
 | 2. We can connect & debug A7 using Jlink successfully (remove the JTAG port-2 Vcc) | Pass
 | 3. Mictor 38 port debug function pass. Trace function is OK | Pass
 | 4. CoreSight debug/trace A7/M7 basic function pass. | Pass
SD controller | 1. Access register case pass; | Pass
 | 2. Fifo mode passed | Pass
 | 3. DMA mode is passed. | Pass
 | 4. IO voltage change. | not_done
SRAM | 1. boot with sram_main case pass; | Pass
 | 2. Access sram_bb pass; | Pass
 | 3. sram transfer data with bb pass; | Pass

## Slide 15: Bring up detail list - 11
CGU&RGU | 1. CGU gate off all blocks will save 91mA (9V) | Pass
 | 2. RGU reset all blocks will save 76mA | Pass
 | 3. both CGU and RGU will save total 141mA | Pass
 | 4. HEVC power on will increase 13mA, gate clock can save 12mA | Pass
 | 5. ISP power on will increase 20mA, gate clock can save 19mA | Pass
 | 6. memory LS/DS/SD for SRAM/BOOT_ROM/HEVC/H264/JPEG/DISP/SMMU save less than 1mA | Pass
MIPI_TX | 1. spi rd/wr register is ok. | Pass
JPEG | 1. JPEG encode 1920x1080/yuv420/8bit picture passed | Pass
 | 2. JPEG decode 256x128, 3840x2160 picture passed | Pass
H264 | 1. Read/write register passed. | Pass
 | 2. H264 encoder encode in ALL intra and IPPIPP mode passed. | Pass
 | 3. H264 decoder decode passed. | Pass
OTP | 1. read/write register ok. | Pass
 | 2. program through CPU is OK. | Pass
NOC | 1. Test the frequency of NOC. 300Mhz, 500Mhz, 600Mhz and 800Mhz is OK. | Pass

## Slide 16: Bring up detail list – 12
CCI |  | not_done
TZC |  | not_done
CAN | CAN0~3 tx/rx basic function pass | Pass
GPIO | 1. Access register is OK. | Pass
 | 2. Till now all the path of digital PADs with share-function, DDR, TYPEC and MIPI2/4/6/7 channel are tested, that is to say, the substrate connection is no problem. | Pass
Power | 1. test VDD_0v9 leakage power, CA7/CEVA/DDR controller dynamic power, | Pass

## Slide 17: Go to Validation stage
No. | To do list
1 | Debug problem that CPU read/write EMMC device but with a error flag
2 | SPI DMA mode
3 | I2C DMA mode.
4 | SD IO controller IO voltage change
5 | CCI
6 | TZC
7 | MIPI_RX: 1.2G input test
8 | eMMC HS200 mode
9 | SD HS200 mode
10 | I2S RX mode