## Slide 1: Low Delay Implementation

## Slide 2: Specification
Current Specification
  Input: HDMI ->VIF
  1080P@60fps
  5Mbps~10Mbps
  最多一次重传（+9ms波动）
Potential Issue
  码流错误出现花屏；
    弥补方案：Slice，Intra Refresh以及decoder自身的Error concellment做一些弥补；
  重传导致的刷屏和丢帧；
    弥补方案：丢帧让display和decoder回到平衡，将延时拉回；
  BigPicture导致的刷屏和丢帧；
    弥补方案：预检测出来，提高QP，压缩码率，导致质量会有所损失；

## Slide 3: Scheme
Slice Level Display
  2ms/ slice
  8ms(4 slice to display)
 | ` |  |  | 实测8.5 | one slice | 解码端 | 
 | T0 (ms) | T1 (ms) | T2 (ms) | T3 (ms) | T4 (ms) | T5 (ms) | Total (ms)
一次性正确，无需重传 | 0.02 | 0.99 | 0.50 | 8.50 | 2.00 | 8.00 | 20.00
重传一次“正确” | 0.02 | 0.99 | 0.50 | 8.5 + 9 | 2.00 | 8.00 | 29.00
重传所导致的问题：
  重传导致的刷屏和丢帧；
  弥补方案：丢帧让display和decoder回到平衡，将延时拉回；

## Slide 4: Veloce DB Requirements
Stage1
  SPI transmission is used to substitute BB transmission, only for video evaluation.

## Slide 5: Veloce DB Requirements
Stage2
  Delay Monitor

## Slide 6: Key points
1. Low delay encoding: confirmed
2. Send cmd to BB( 1CMD/0.5ms): confirmed
3. Send cmd to Dec: need try
  Need confirmed:
    dec wrptr can be updated any time? Or interrupt to update it.
    Sps/pps need 1024 bytes? If need 1024, sps/pps + padding zero can work?
    How to flush decoder finish one frame if the rest bytes is not enough(such 3 bytes)?
    Does slice affects the intra refresh?
  Scheme:
    BB sync the cmd  CPU parser the block and move the data into sram  inform to decoder
4. The start point of starting display: need try
  Scheme:
    Start timmer after launch decoding the FIRST frame 4 ms  launch display
5. Correct the phase error betweeen decoder and display
  Need confirmed
    Display can update the blank time to adjust the display vsync point
  Scheme:
    If the phase error > 2ms, then update blank time to adjust vsync point.

## Slide 7: Dec Key Points
在随机接入的时候，直到Decoder找到正确的sps/pps为止；
找到sps/pps后，

## Slide 8: Potential Issue & Solution
SPS/PPS要定期的发送，为了随机接入；
  SPS/PPS后面的帧如果插入I帧，那么质量可能会受到影响；（实现后要查看效果）
  SPS/PPS后面的帧如果不插入I帧，那么至少要经历16帧（0.25s) 后，才能恢复正常；
解码过程中，如果收到错误的SPS/PPS，被识别的话可以丢掉不受影响，不被识别的话，可能会使图像花屏；（需要造这个case测试一下）
解码过程中，如果收到错误的帧码流，那么必然会出现图像花屏（大约需要16帧（IntraRefresh)后才能恢复）；
需要专门测试一下场景切换帧（Big Picture）可能对延时抖动带来的影响;（我们测试的几个场景中，HEVC对场景切换帧还是表现比较好的，但是还是要更多的场景检验）

## Slide 10: HEVC Based Low-delay

## Slide 11: Decoder End Program

## Slide 12: Potential Issue And Methods
码流错误: （产品中必须考虑到这些问题）
  虽然码流错误，但是源vsync与Display的Vsync的相位差保持不变，应该还好；
  顶多刷屏；
  我们采用的slice的方式也起到了一定的作用；
  近距离的时候发生码流错误的概率较少；
重传导致的延时
  丢帧机制（也就是卡顿）

## Slide 13: Review HEVC Decoding
Configure Registers
BS_PARAM and BS_OPTION
BS_OPTION: explicit_end flag
  Interrupt Mode: explicit_end flag = 0
  PicEnd Mode: explicit_end flag = 1
    Interrupt Mode can change to PICEND mode any time.
    But PICEND mode change to Interrupt mode, only if idle state.

## Slide 15: Extended
Low Delay Audio

## Slide 16: Screen Tearing

## Slide 17: V-Sync/G-Sync/Free-Sync
V-Sync: 固定帧率，为了防止Tearing, 只显示已经render好的帧；
G-Sync/Free-Sync：adaptive 帧率和刷新率；