## Slide 1: USB3.0 Subsystem Review
IP Owner: Hao Sun

## Slide 2: Content
Introduction
SoC Connection
IP check

## Slide 3: Introduction

## Slide 4: SoC Connection

## Slide 5: IP check
Subsystem Block Diagram
Register map & Port description
IP Config
DDR Band Width & Access latency
Verification
Synthesis & Formality
Board
PHY ATE test
Conformance test
IP bring up
Check list

## Slide 7: Register map
Base Address | Controller CSR address index | Register Type | 1MB
0x6050_0000 | 0x0_0000 to 0x0_7FFF | xHCI Registers(Xxxxx) | 32KB
 | 0 to CAPLENGTH -1 | eXtensible Host Controller Capability Reg | 
 | CAPLENGTH to RTSOFF -1 | HOST Controller Operational Reg | 
 | RTSOFF to BDOFF -1 | Controller Runtime Reg | 
 | DBOFFF to (xECP*4-1) | Doorbell Reg | 
 | xECP*4 to 0x0_7FFF | xHCI Extended Capabilities | 
 | 0x0_C100 to 0x0_C6FF | Global Registers (Gxxxx) | 1.5KB
 | 0x0_C700 to 0x0_CBFF | Device Registers (Dxxxx) | 1.25KB
 | 0x0_CC00 to 0x0_CCFF | USB 20 OTG and Battery Charger Register | 256B
 | 0x0_CD00 to 0x0_CFFF | Unused/Aliased | 0.75KB
 | 0x4_0000 to 0x7_FFFF | Internal RAM0 - Debug Access | 256KB
 | 0x8_0000 to 0xB_FFFF | Internal RAM1 - Debug Access | 256KB
 | 0xC_0000 to 0xF_FFFF | Internal RAM2 - Debug Access | 256KB
 | Subsystem Slave Address index | Register Type | 64KB
0x6060_0000 |  | PHY CR address index | 36KB
 | 0x0000 << 2 to 0x1N42 << 2 | SS Function Control Registers | 
 | 0x0000 to 0x7D08 |  | 
 | 0x2000 << 2 to 0x200D << 2 | HS Function RO Control Registers | 
 | 0x8000 to 0x8034 |  | 
 | 0x2010 << 2 to 0x201F << 2 | HS Function R/W Control Registers | 
 | 0x8040 to 0x807c |  | 
 |  | USB30 subsys registerfile index | 28KB
 | 0x9000 to 0x901c | USB30 Controller Pins Ctrl Registers | 
 | 0x9020 to 0x902c | Memory Pins Control Registers | 
 | 0x9030 to 0x906c | femtoPHY Pins Control Registers | 
 | 0x9070 to 0x9074 | Debug Control Registers | 

## Slide 8: Top port
IO name | IO | Width | Connection
globa_clk_150m | I | 1 | CGU
globa_clk_24m | I | 1 | CGU
dut_vcc_reset_n | I | 1 | RGU
apb_preset_n | I | 1 | RGU
phy_phy_reset | I | 1 | RGU
dut_interrupt | O | 1 | GIC
dut_host_system_err | O | 1 | GIC
AHB SLAVE |  | BUS | NOC
AXI MASTER |  | BUS | NOC
dut_hub_vbus_ctrl | O | 1 | TOP DIGITAL PAD
dut_hub_port_overcurrent | I | 1 | TOP DIGITAL PAD
DVDD | I | 1 | Power Supply
VDD330 | I | 1 | Power Supply
VDDH0 | I | 1 | Power Supply
VSSA0 | I | 1 | Power Supply
gd | I | 1 | Power Supply
vp | I | 1 | Power Supply
vph | I | 1 | Power Supply
vptx0 | I | 1 | Power Supply
vss | I | 1 | Power Supply
IO name | IO | Width | Connection
ate_test_en | I | 1 | TOP TEST
dut_scan_mode | I | 1 | TOP TEST
dut_dft_en_bus_clk_gated | I | 1 | TOP TEST
dut_dft_en_ram_clk_gated | I | 1 | TOP TEST
ram_0_test | I | 1 | TOP TEST
ram_1_test | I | 1 | TOP TEST
ram_2_test | I | 1 | TOP TEST
Scan Interface |  | BUS | TOP TEST
JTAG |  | BUS | TOP TEST
Boundary Scan |  | BUS | TOP TEST
ID0 | IO | 1 | TOP ANALOG PAD
ref_pad_clk_p | I | 1 | TOP ANALOG PAD
ref_pad_clk_m | I | 1 | TOP ANALOG PAD
resref | IO | 1 | TOP ANALOG PAD
rx0_m | I | 1 | TOP ANALOG PAD
rx0_p | I | 1 | TOP ANALOG PAD
DM0 | IO | 1 | TOP ANALOG PAD
DP0 | IO | 1 | TOP ANALOG PAD
VBUS0 | IO | 1 | TOP ANALOG PAD
tx0_m | O | 1 | TOP ANALOG PAD
tx0_p | O | 1 | TOP ANALOG PAD

## Slide 9: IP Config
Dual-Role Device
Support large DMA bus latency(larger than 2.1us for 1KB SS)
2.0 PHY: 8bit UTMI+
3.0 PHY: 32bit PIPE3
Device: Max 16 endpoints
Rx/Tx MaxPacket Size 1024 Byte
Host: USB2.0/USB3.0 root hub ports 1
Support max 64 device
Support max 32 periodic endpoint

## Slide 10: DDR Band Width & Access latency
 | AXI master
Clk | 150Mhz
Bandwidth | 9.6Gbit
Interface | AXI RW
Data width | 64bit
Burst length | INCR,INCR4,…,INCR256
System latency | Time
ddr4 switch bank max delay | 45ns
1KB data store/read time when ddr4 operates at 1833MHz | 1KB/64bit * 1s/1833MHz = 69.83ns
NOC access latency(600MHz idle) | 50 * 1s/600MHz = 83.33ns
Total access latency | 45ns + 69.83ns + 83.33ns = 198.16ns

## Slide 11
Verification
Synthesis
Formality
PHY only: pass Controller only: debug Top: debug
Verification Status |  | Pattern Number |  |  |  | 
 |  | Planned | Executed | Passed | Failed | Complete Rate
RTL Simulation | Local Sim | 154 | 154 | 154 | 0 | 100.00%
 | SoC-level Sim | 5 |  |  |  | 0.00%
Gate-level Simulation |  |  |  |  |  | 
Gate-level w/ sdf Sim |  |  |  |  |  | 
FPGA |  | 2 |  |  |  | 
Veloce |  | 2 |  |  |  | 
sub system name | total area | memory | phy | inst number | tech lib | note
USB30_TOP | 0.8630 | 0.0999 | 0.5649 | 271,719 | 7T | w phy/pad

## Slide 12: Board

## Slide 13: PHY ATE test

## Slide 14: Conformance test
Use Keysight’s solution
Change PHY’s parameter to meet the requirement

## Slide 15: IP bring up
PHY Power on Reset
Controller mode switch
Host mode initial
Device mode initial

## Slide 16: PHY Power on Reset

## Slide 17: Controller mode switch
Register GCTL[13:12]
Switching from Device to Host
1.Reset the controller using GCTL[11](CoreSoftReset).
2.Set GCTL[13:12](PrtCapDir) to 2’b01(Host mode).
3.Reset the host using USBCMD.HCRESET.
4. Host mode initial.
Switching from Host to Device
1.Reset the controller using GCTL[11](CoreSoftReset).
2.Set GCTL[13:12](PrtCapDir) to 2’b10(Device mode).
3.Reset the device by setting DCTL[30](CSftRst).
4. Device mode initial.

## Slide 18: Host mode initial

## Slide 19: Device mode initial

## Slide 20: Check List
Sub-CLASS | Items | Description | Status | Comment
Document | IP Release Note | Describes the content of IP package,and the updates to last version. | done | Controller 3.10a, femtophy 4.04a
 | IP datasheet | Must include full register map and description, I/O structures, block description and sub IP partitioning. | done | 
 | IP DFT/ATE test spec (mostly for AMS IPs) | Must define what it contains (must include description of test protocol for special test modes) | done | ate app note
 | IP integration Manual | Requiremnt for IO/Clock/Rest/DFT; IP block digarm; Port descriptions and connections in SOC | done | 
 | IP verfication spec and report | Bench and test cases descriptions; code coverage; functional coverage | pending | CASE:8000976677 no code coverage,functional coverage
 | IP programing guide | Description of IP bring up, Register settings for different modes | pending | CASE:8000976636
 | IP data flow /floorplan/TOP diagram | Description of connections among sub-blocks, memories, backend floorplan | done | 
 | IP package/PCB guide | Description of Ball assignment/PCB layout | done | CASE:8000975825,synopsys offer PCB guidline and visual review when it is near completion , but no PCB reference design,
Design | IP configure | Include IP feature configure | done | 
 | RTL | RTL code, netlist, behavior models | pending | netlist not ready
 | Design File List | File list for Chip test bench build. | done | 
 | Memory list | Memory configure list | done | 
 | IP fake model | dummy IP subsystem top | done | 
 | IP unit verification environment | Bench,test cases, scripts ,logs, coverage reports, failed case,issue | done | 
 | IP synthesis environment | Scripts,SDC,netlist,logs, report | pending | netlist not ready
 | IP Formal check environment | Scripts, report | pending | formality fail
 | IP ATPG environment | Scripts, report | pending | only have phy atpg
 | IP verification Plan | Include SOC level/Veloce/FPGA verification test report. | pending | soc level old version 1 case pass, new version doing
 | IP NLS Maturity Check | release netlist, chiplevel backend SDC | pending | netlist not ready
Software | IP SW driver | Software driver for application | pending | CASE: 8000976297