## Slide 1: HEVC Codec IP Review
Jialiang Liu / Xing Yuan
2017-11-15

## Slide 2: Contents
IP Features
Block Diagram
  Key internal modules
  Interfaces
Performance & Target Perf.
Sign Off
Buffers and BW
Program & Workflow
Codec System Delay
Key Features

## Slide 3: Feature
HEVC Encoder
  Main/Main10 Profile @ L5.0 High Tier
  8bit/10bit sample precision
  Max Performance:
    4K@30fps @ 400MHz
  Max Resolution: 8192x4096
  CBR, ABR, VBR rate control
  I/P/B frame types
  Flexible GOP setting( 8 kinds of GOP structure )
  ROI / QP Mapping / Mode Mapping
  Noise Reduction
  Sub-FrameSync (low delay tool)
  Intra-Refresh (low delay tool )
  Reference Compression
  High Complicated RDO
  YUV 420/422
  HEVC Tools
    CU Size: 64x64, 32x32, 16x16, 8x8
    PU Size: 32x32, 16x16, 8x8
    TU Size: 32x32, 16x16, 8x8, 4x4
    Deblocking/SAO
    WPP/ MultiSlice
    Lossless Coding
    Transform skip
    Search Range: [+/-128H, +/-64]

## Slide 4: Feature
HEVC Decoder
  Compatible with HEVC Main/Main10 @ L5.0 Main-tier
  High Performance CABAC
  Reference Compression
  Robust Error Concealment

## Slide 5: Block Diagram
Key Internal Modules
  V-CPU
    32bit processor
      Enc/dec high level syntax-SPS /PPS/SH
      Communicate with Host
      Give params/info to V-Core
  V-Core
    BPU
      Packing/parsing of coded slice data
      Cabac
      CTU/CU/PU/TU-level parameter derivation
    VCE
      ME/RDO/T/Q/IT/IQ/LF/SAO/FBC/FBD/BWB

## Slide 6: Block Diagram
Interfaces
  Interrupt
  Idle
  AXI Bus
  APB Bus
  Low delay
  power control

## Slide 7: Performance Requirement
3840x2160@30fps + 1080P@30fps @ 550MHz ( with 50Mhz margin)
Encoder ( cclk @ bclk 333MHz ) |  | Decoder ( cclk @ bclk 333MHz) | 
4K @ 30 fps, IPPP, 8bit | 400 MHz, (no margin) | 4K @ 30fps, IPPP, 8bit | 300MHz (no margin)
4K @ 30 fps, IBBB, 8bit | 410 MHz, (no margin) | 4K @ 30fps, IBBB, 8bit | <400MHz (estimated)
4K @ 30 fps, IPPP, 10bit | 410 MHz, (no margin) | 4K @ 30fps, IPPP, 10bit | 300MHz( no margin )
4K @ 30fps, IBBB, 10 bit | 410 MHz, (no margin) | 4K @ 30fps, IBBB, 10bit | <400MHz( estimated)
Cabac (Encoder) ( bclk ) | Cabac(Decoder) ( bclk )
~ 2 bin / cycle (500Mbps @ bclk 333MHz, cclk 410MHz) | ?(未统计)

## Slide 8: SignOff
Corner
  7T, SVT,C35
  ssgwc0p81vn40c
Constraints
  30% clock uncertainty
Power Domain
Area | 
PR Area | 6,724,870
DC Area | 3,905,299
Memory Area | 1,367,114
Instance | 3,035,098
Memory Size | 3,367,584(bit)
Frequency | 
PCLK | 150MHz
BCLK | 300MHz
CCLK | 360MHz
ACLK | 360MHz

## Slide 9: SignOff
Clocks
  4 Clock domains
    CLK_AXI_500_G0 / CLK_CORE_HEVC/ CLK_BPU_HEVC / CLK_CFG_150_G7
    False path between each other
  CCLK and ACLK are one clock source

## Slide 10: Buffers in DDR
Code Buf : 1 for all instances
  V-CPU running code
Work Buf : 1 for each instance
  Stores the information during encoding/decoding process. ?
Temp Buf : 1 for each instance
  Top line for IP, Top line for Debloking, Neighbor infor for RDO, and CABAC
  Size: 128KBtye for Enc, 3MByte for Dec
Bit stream Buf:
Frame Buf:
  Uncompressed ( linear )
  Compressed
Collocated MV:
Subsample Frame:
  For IME

## Slide 11: BandWidth
4K @ 30fps Encoding, 3P/4B for 10bit
4K @ 30fps Decoding, 3P/4B for 10bit
  Decoder BW < Encoder BW
Frame Type | 8bit | 10 bit
P | 900MBps | 1350MBps
B | 1170MBps | 1740MBps

## Slide 12: FB Format
Pixel Layout
  0: 8bit mode
  1: 16bit mode, LSB padding
  2: 16bit mode, MSB padding
  3: 32bit mode, LSB padding
  4: 32bit mode, MSB padding
Frame Layout
  Source Image
    8 bit/ 10 bit
    YUV420/YUV422 ( down sample to YUV420 internally )
    Planar, Semi-planar, Compressed (CF50)
  Rec Image
    8 bit/ 10 bit
    YUV420
    Planar, Semi-planar, Compressed (CF100)

## Slide 13: FB Format Requirement for ISP/VIF
For ISP/VIF
Mode | Bit depth | Pixel Format | Layout on 128bit bus | Layout on DDR | YUV | For IP | 主路 | 从1 | 从2
1 | 8 | 1B/1P | [MSB] P15 … P2 P1 P0[LSB] | Planar | YUV420 | HEVC/H264/JPEG/Display | √ | √ | √
2 | 8 | 1B/1P | [MSB] P15 … P2 P1 P0[LSB] | Planar | YUV422 | JPEG | √ | √ | √
3 | 8 | 1B/1P | [MSB] P15 … P2 P1 P0[LSB] | Planar | YUV444 | JPEG | √ | N | N
4 | 8 | 1B/1P | [MSB] P15 … P2 P1 P0[LSB] | Semi-planar | YUV422 | Display | √ | N | N
5 | 8 | 1B/1P | [MSB] P0 P1 P2 … P15[LSB] | Planar | YUV420 | CF50 | √ | N | N
6 | 10 | 4B/3P（ Valid bits in LSB ） | [MSB] P11 … P2 P1 P0[LSB] | Semi-planar | YUV420 | HEVC/Display(w/o scalling/mirror/rotation) | √ | N | N
7 | 10 | 4B/3P（ Valid bits in LSB ） | [MSB] P11 … P2 P1 P0[LSB] | Semi-planar | YUV422 | Display | √ | N | N
8 | 10 | 2B/1P ( Valid bits in MSB ) | [MSB] P7 … P2 P1 P0[LSB] | Semi-planar | YUV420 | Display( w Scaling/mirror/rotation) / Jpeg for 12bit encoding / HEVC | √ | N | N
9 | 10 | 2B/1P ( Valid bits in MSB ) | [MSB] P7 … P2 P1 P0[LSB] | Semi-planar | YUV422 | Jpeg for 12bit encoding / HEVC | √ | N | N
10 | 10 | 2B/1P ( Valid bits in MSB ) | [MSB] P7 … P2 P1 P0[LSB] | Semi-planar | YUV444 | JPEG for 12bit encoding | √ | N | N
11 | 10 | 2B/1P ( Valid bits in LSB ) | [MSB] P0 P1 P2 … P7 [LSB] | Planar | YUV420 | CF50 | √ | N | N

## Slide 14: Endian
Only LITTLE endian is required in Sirius.
  16 endian modes

## Slide 15: AXI Bus
Two axi buses
  Pri-AXI
    Access Code Buf, Work Buf, Frame Buf, BitStream Buf, and the bufs except Temp buf.
  Sec-AXI
    Optional, to access on chip sram
    Temp Buf
AXI requests efficiency to DDR
  Refer to <LeiYu.ppt>

## Slide 16: Program & Workflow
Encoding Flow

## Slide 17: Program & Workflow
Decoding flow

## Slide 18: Codec System Delay
Issue:
  Can NOT generate interrupt signal ½ or 1/N picture encoding.

## Slide 19: Quality Evaluation
HEVC vs H264
Chart: Basketball 1080P HEVC_H264_Frame_Bitrate with constant QP

## Slide 20
Chart: Pedestrian 1080P HEVC_H264_Frame_Bitrate with constant QP

## Slide 21: Quality summary

## Slide 22: Key Features
Low-delay encoding
  Signal: i_ipu_new_frame, i_ipu_end_of_row, i_ipu_current_buff[2:0]

## Slide 23: Low_delay Timing

## Slide 24: Bitstream Transfer with Baseband
1. DJI Products
2. Timing save

## Slide 25: Key Features
Intra Refresh
  Enabled in non-intra picture
  For error robustness

## Slide 26: Recovery scheme

## Slide 27: Intra Refresh Config
Register
1> Intra_Refresh_Mode, 2bits
0– No intra Refresh ; 1- Row ; 2- Column ; 3- step size in CTU
2> Intra_Refresh_Arg, 16bits
num consecutive CUT Rows in Mode 1 ;
num consecutive CUT Columns in Mode2 ;
Step size in CTU for Mode3

## Slide 28: Image quality with Intra Refresh

## Slide 29: Key Features
Noise reduction
  (noise reduction是怎么回事儿）
  质量如何？
  DuHua and Hikvision smart H265+
  Sirius HEVC encoder ?

## Slide 30: End
Thanks
Q&A