## Slide 1: M7 Sub & CS Review
Zhang Hao

## Slide 2: Content
M7 Subsystem
  Diagram
  Introduction
  CS
  Diagram
  Introduction
  SIM

## Slide 3: M7sub - Diagram

## Slide 4: M7sub – M7core
Parameter | Value | Description
ITCM | 128KB | Itcm size
DTCM | 64KB | Dtcm size
ICACHE | 16KB | Icache size
DCACHE | 16KB | Dcache size
FPU | 2 | Both single & double precision
ETM | 2 | Data & Instruction
INITVCTOR | Register | Configured by register
INT NUM | 160 | Interrupt number

## Slide 5: M7sub – QSPI

## Slide 6: M7sub – QSPI
Mem/Reg Definition
  cmd mem (APB)
  intr high/low mem (APB)
  cmd addr mem (APB)
  rd/wr inst high/low reg (AHB)
Used to active SPI command
Reconfigure the instruction word
Configure the addr needed by SPI cmd
Reconfigure the instruction word (rd/wr)
sel
instruction word

## Slide 7: M7sub – QSPI
Instruction Structure
  High Word (19bit)
  Low Word (32bit)
  Address (32bit)
  Data (32bit)
High word =
{
bus width, //2 bits
Mode bit width, //2 bits
Tag, //1 bit, 0-APB, 1-AHB
Dir, //1 bit, 0-Read, 1-Write
Cmd bit width, //2 bits
Cmd, //8 bits
Mode cycle //3 bits
}
*bit width : 00-1bit, 01-2bit, 10-4bit 11-reserved
Low word =
{
mode, //2 bits
Dummy cycle, //5 bits
Data bit width, //2 bits
Data cycle, //9 bits
Addr bit width, //2 bits
Addr cnt sel, //2 bits <address bits switch>
Cmd quad mode, //1 bit
Addr quad mode, //1 bit
Mode quad mode, //1 bit
Data quad mode //1 bit
}
*bit width : 00-1bit, 01-2bit, 10-4bit 11-reserved

## Slide 8: M7sub – QSPI
Instruction Structure
  20h – sector erase
cmd: 20h
addr: 24bit
Others : no
inst_high =
{
2’b0, //bus width, //2 bits
2’b0, //Mode bit width, //2 bits
1’b0, //Tag, //1 bit, 0-APB, 1-AHB
1’b1, //Dir, //1 bit, 0-Read, 1-Write
2’b0, //Cmd bit width, //2 bits
8’h20, //Cmd, //8 bits
3’b0 //Mode cycle //3 bits
}
Inst_low =
{
2’b0, //mode, //2 bits
5’b0, //Dummy cycle, //5 bits
2’b00, //Data bit width, //2 bits
9’b0, //Data cycle, //9 bits
2’b0, //Addr bit width, //2 bits
2’b01, //Addr cnt sel, //2 bits <address bits switch>
1’b0, //Cmd quad mode, //1 bit
1’b0, //Addr quad mode, //1 bit
1’b0, //Mode quad mode, //1 bit
1’b0 //Data quad mode //1 bit
}

## Slide 9: M7sub – QSPI
Operation Flow

## Slide 10: M7sub – Peripheral with DMA
Simple Diagram

## Slide 11: M7sub – Pin Share
How to use?
  sirius_pins_vxxx.xlsx
  sirius_top_global_register.xlsx
  pin_share.c

## Slide 12: CoreSight - Diagram
1. Access Part
2. TimeStamp
3. Trigger Control Part
4. Trace Source
5. Trace Link
6. Trace Sink
7. APB Interconnect Bus

## Slide 13: CoreSight - DAP

## Slide 14: CoreSight - APBIC

## Slide 15: CoreSight – Rom Table

## Slide 16: CoreSight – Trigger

## Slide 17: M7Sub - Sim
Local env
  execution_tb
  ( config_check / itm_trace / etm_trace / mpu / reset / rom_table / debug / interrupt ect. )

## Slide 18: M7Sub - Sim
Local env
  ram_integration_tb
  ( Icache / Dcache / ITCM / DTCM )

## Slide 19: M7Sub - Sim
SoC env

## Slide 20: CoreSight - Sim

## Slide 21: CoreSight - Sim
hello_world
discovery
ram_integration
memap_check
partlibcheck
cxsystem_check
cti_channel
7/14 = 50%

## Slide 22: Q&A
Thanks. Q&A