## Slide 1: Sirius PCIe Review
Jiajie Zhang

## Slide 2: CONTENT
PCIe Protocol
License IP
Arch
Integration
Simulation
Backend
Limitation
Ate Test
Bring Up
Reference

## Slide 3: PCIe Protocol
PCI Express Layer

## Slide 4: PCIe Protocol
Root Complex / Switch / Endpoint

## Slide 5: License IP: Synopsys PCIe dual mode (DM) controller
Features
  All non-optional features of the PCI Express 2.0
  Root complex / Endpoint
  x2 Gen1, Gen2 lanes
  32-bit Internal Datapath Operating at 125 or 250 MHz
  AXI4 bridge
  Internal Address Translation Unit
  Two Embedded DMA

## Slide 6: License IP: Synopsys PCIe 2 PHY
Features
  Implement complete PCI Express 2.0 physical layer capability for 5-Gbps operation.
  PIPE3-compliant transceiver interface, mapped onto 2 lanes.

## Slide 7: Architecture

## Slide 8: Integrator Logic
Connect controller and phy through standard PIPE interface
Implement PCIe external registers
External memory replace
Hand-Placed logic

## Slide 9: Initialization steps
Immediately upon powerup the DM controller goes into either EP mode or RC mode, depending on the state of the device_type register.

## Slide 10: SIMULATION
LOCAL SIM
SOC SIM
EMU SIM

## Slide 11: SIMULATION: Local Sim
Controller: DWC PCIe IIP - VTB

## Slide 12: SIMULATION: Local Sim
PHY
  Hard macro behavior / gate-level model
  Receiver detection
  Ate test pattern

## Slide 13: SIMULATION: SOC Sim
VTB reuse
  Replace pcie_iip_device with sirius testbench
  Interface to testbench.u_sirius_top.sirius_sub_3_inst.pcie_iip_device_inst
  Replace tb sequence with firmware

## Slide 14: SIMULATION: SOC Sim
Connect two sirius testbench using pcie link
  Easy to replace rtl to netlist and run post sim

## Slide 15: SIMULATION: EMU Sim
PCIe controller connect to Veloce model by PIPE3 interface
  RC database / EP database

## Slide 16: BACKEND: SYN
Integrate constraint of Controller & PHY
Macro/Black Box area: PHY + PAD + MEM =0.61 + 0.14 + 0.17 =0.92

## Slide 17: BACKEND: BUMP&&BALL
The length match between diff pairs are guaranteed by substrate and PCB design

## Slide 18: Limitation
LINK_CONTROL_LINK_STATUS_REG - PCIE_CAP_COMMON_CLK_CONFIG bit
Separate Refclk Architecture
  using an on-chip clock source, tie the off-chip source to ground
Common Refclk Architecture
  RC: ref_alt_clk_p/m for PCIe PHY and output to EP
  EP: ref_pad_clk_p/m
Common Refclk Architecture (ssc support)
Separate Refclk Architecture

## Slide 19: ATE_TEST
BERT test

## Slide 20: Bring Up
Monitor out logic
Link up interrupt
Feature test
Performance test
PCIe | function validation | (RC/EP) Monitor out to PAD
 |  | (RC/EP) CLK frequency/RSTN check
 |  | (RC/EP) register default value check and read/write
 |  | (RC/EP) Link up interrupt check
 |  | (RC/EP) device id and vendor id access
 |  | (RC/EP) msix transaction test
 |  | (RC/EP) atu feature test
 |  | (RC/EP) atu bypass feature test
 |  | (RC/EP) dma ll feature test
 |  | (RC/EP) dma non ll feature test
 |  | (RC/EP) physical layer reset test
 |  | (RC/EP) link speeds test
 |  | (RC/EP) hot reset test
 |  | (RC/EP) link disable state test
 |  | (RC/EP) DDR access through remote pcie
 |  | (RC/EP) DMAC access axi slv
 |  | (RC/EP) Hot-Plug behavior
 | performance validation | (RC/EP) TOP DMAC and PCIE edma
 | physical validation | Eye Diagram

## Slide 21: Reference
About spec
${git_server}/pub_doc/standard/pcie
About doc
${git_server}/sirius_doc/IP/PCIE