## Slide 1: GMAC Review
Yang Lei

## Slide 2: CONTENT
Introduction
Integration
Verification

## Slide 3: Introduction

## Slide 4: Integretion
Feature:
■ Programmable 10/100 or 1000 Mbps operation ■ Full- or half-duplex operation
■ Reduce Gigabit Media Independent Interface (RGMII) for 1Gbps ■ MDIO interface for PHY configuration and management

## Slide 5: Integration
■ Area: 0.04mm
■ Performance: meet 1000Mb/s
■ Clk:

## Slide 6
1.Store the frame to the memory.
2.Associate the TXBD in the Gbethernet MAC core with packet written to the memory (length, pad, crc, etc.).
3.Enable the TXEN bit in MODE register to 1.
Frame transmitter
TX Buffer Descriptors

## Slide 7
1.Set the receive buffer descriptor to be associated with the received packet and mark it as empty.
2.Enable the RECEN bit in the MODE register to 1.
Frame Reception
RX Buffer Descriptors

## Slide 8
RGMII TX & RX interface
rgmii tx interface
rgmii rx interface

## Slide 9
RGMII & RMII interface
rgmii rx interface

## Slide 10: Bus Interface
■ Wishbone bus
Wishbone bus multi_read

## Slide 11: Bus Interface
■ Wishbone bus
Wishbone bus multi_write

## Slide 12: Bus Interface
■ Wishbone 2 AHB
■ Wishbone 2 AXI is better

## Slide 13: Sim
■ Local sim
./rtl_sim –d gbeth_top –r gbeth_receiver_tcs –deb
./rtl_sim –d gbeth_top –r gbeth_transmitter_tcs -deb
./rtl_sim –d gbeth_top –r gbeth_half_duplex_tcs –deb
./rtl_sim –d gbeth_top –r gbeth_loopback_tcs –deb
./rtl_sim –d gbeth_top –r gbeth_wishbone_master_tcs
./rtl_sim –d gbeth_top –r gbeth_receiver_tcs
–def GBETHERNET_RGMII_IMPLENMENTED –deb
./rtl_sim –d gbeth_top –r gbeth_transmitter_tcs
–def GBETHERNET_RGMII_IMPLENMENTED –deb

## Slide 14: Sim
■ Veloce sim
■ Soc sim
eth_rgmii_phy.v
velrun –do run.do.linux –exe ./tb-dpi.veloce
run epgm

## Slide 15: EMMC Review
Yang Lei

## Slide 16: CONTENT
Introduction
Integration
Programming
Sim

## Slide 17: Introduction

## Slide 18: Introduction

## Slide 19: Integration
Feature:
■ Supports eMMC protocols including eMMC 5.1 ■ Supports tuning
■ Supports Supports data transfer types for CPU, SDMA, ADMA2, ADMA3
■ Supports legacy, High Speed SDR, HS200 speed modes

## Slide 20: Integration
■ Area: 0.03mm
■ Performance: meet HS200 (200MB/s)
■ Clk

## Slide 21: Programming

## Slide 22: Sim
■ Local sim
test_cust_card_init_wr_rd
test_cust_card_wr_rd_sdma_mode
test_cust_card_wr_rd_adma2_mode
test_cust_card_wr_rd_adma3_mode
test_cust_card_wr_rd_half_duplex_mode
❑ AMBA VIP
❑ EMMC SVT VIP
❑ TEST CASE

## Slide 23: Sim
■ Soc sim
❑ EMMC SVT VIP integration
reference to “VC VIP eMMC UVM User Guide”
■ Veloce sim
❑ EMMC_HEX
preload_CID.hex
preload_CSD.hex
preload_OCR.hex
preload_EXT_CSD.hex
preload_user.hex
preload_gp.hex

## Slide 24: SRAM_TOP Review
Yang Lei

## Slide 25: Architecture

## Slide 26
DMAC Review
Yang Lei

## Slide 27: CONTENT
Introduction
Integration
Application Analysis

## Slide 28
Introduction
The dma controller is a highly configurable, highly programmable, high performance, multimaster multichannel DMA Controller with AXI as the bus interface for data transfer.
Feature:
■ Up to 8 channels, one per source and destination pair ■ Up to 2 AXI master interfaces
■ Memory-to-memory, memory-to-peripheral, peripheral-to-memory, and peripheral-to-peripheral DMA transfers

## Slide 29: Integration
TOP DMAC
■ 2 AXI 4 master interfaces, each outstanding num 4 ■ 2 channels, each channel buffer depth 64
■ area: 0.09 mm2
■ performance: 4Gb/s

## Slide 30: Integration
■ 1 AXI 4 master interfaces, outstanding 8 ■ 4 channels, each channel buffer depth 32
■ area: 0.1mm2
■ performance: 4Gb/s

## Slide 31: Flow control

## Slide 32: Application Analysis
channel num | channel buffer depth | total buffer num/outstanding | NOC outstanding | performance | area
4 | 32 | 128/8 | 8 | 4Gb/s | 0.1mm
4 | 64 | 256/16 | 8 | 5.5Gb/s | 0.15mm
1 | 128 | 128/8 | 8 | 6Gb/s | 0.1mm
4 | 128 | 512/32 | 8 | 6Gb/s | 0.25mm
4 | 256 | 1024/64 | 16 | 9Gb/s | 0.35mm

## Slide 33: I2S Review
Yang Lei

## Slide 34: Protocol

## Slide 35: DMA interface