## Slide 1: HDMI design review
Huibo Zhong 2017 11.20

## Slide 2: Profile
1. video timing introduction
2. hdmi design in Sirius

## Slide 3: 1.VIDEO TIMING
Hblank, Hactive
Vblank, Vactive
FPS
Pixel clock = (Hblank+Hactive)*
(vblank+Vactive) * FPS

## Slide 4: 1. VIDEO TIMING
Hblank:
Hfront, Hsync(HSW),
Hback
Vblank:
Vfront, Vsync(VSW)
Vback

## Slide 5: 1. Video timing
Polarity
Interlace
RGB, YUV
Color depth

## Slide 6: 2. Hdmi design in sirius
Feature:
1. HDMI1.4, video up to 4k@30fps, RGB/YUV, deep color support
2. HDCP1.4
3. AUDIO. Up to 192kbps, serial and parallel interface in sirius
4. edid mem inside option

## Slide 7: Edid mem inside option
19 pin type A connector
5V system power
HPD

## Slide 8: hdmi rx controller diagram

## Slide 9: PHY diagram.

## Slide 10: audio pll Interface
ocfg_audpll_mux_cts : 20bit input icfgclk
ocfg_audpll_mux_n : 20bit input icfgclk
O_ctsn_valid : toggle when cts/n change
REQUESTCLK to replace tmdsclk
4.096Mhz ~ 24.576M , 1000PPM

## Slide 11: audio pll Interface

## Slide 12: Audio interface: parallel
L-PCM and compressed audio
One Bit Audio – DSD
Compressed One Bit Audio –DST
HBR Compressed Audio

## Slide 13: Audio interface, serial
Data repeater between HDMI and DPTX
Data repeater between HDMI and i2s

## Slide 14: Audio interface:parallel

## Slide 15: Video interface
To video interface hdmi’s data path

## Slide 16: Video interface

## Slide 17: Syn and sim
Area:
Phy+controller : 1.23
Local sim env
Soc sim env
 |  | area
RXPHY |  | 0.859
I/O |  | 0.259
total |  | 1.118

## Slide 18: ATE test
Internal long bist

## Slide 19: Bring up plan

## Slide 20: Thank you